## Slide 1
COURSE · INFORMATION THEORY AND CODING
Information and Message
Lecture 1 · Science and Subject of the Discipline

## Slide 2
WHY IT MATTERS
Information Theory All Around Us
Information — alongside matter and energy — is one of the fundamental essences of the world
Mathematical formalization: R. Hartley and C. Shannon, first half of the 20th century
One of the greatest achievements of 20th-century science — on par with the theory of relativity
Underpins technologies you use every single day
File Compression (ZIP)
Audio / Video Codecs
QR Codes, Barcodes
Satellite Communication
Hook question for the class: "How much information is in the sentence ‘The Volga flows into the Caspian Sea’?"
Notes: Open with the provocative question before showing this slide. Let 2-3 students answer: information depends on the recipient. Then connect to everyday technologies (ZIP, codecs, QR, satellites).

## Slide 3
FOUNDATIONAL CONCEPTS
Information Is an Undefinable Concept
A strict definition through simpler concepts is impossible without circularity
Mathematical analogy: "point" and "line" are also undefinable primitive concepts
For such concepts we formulate properties and axioms, not further reductions
We introduce information as a primitive concept and study it via its properties and relations
Concepts of the Same Type
Point (geometry)
Line (geometry)
Information (information theory)
Set (set theory)
Notes: Let students try to define "information" themselves first — it almost always ends in circularity. Draw the parallel with undefinable concepts in geometry.

## Slide 4
A KEY DISTINCTION
Message and Information Are Not Synonyms
"This message gives me no information" — the message exists, the information does not
Message: a concrete, material carrier — a sequence of signals, letters, or sounds
Information: what the recipient extracts from a message through understanding it
The correspondence between message and information is not one-to-one
(abstract) information is transmitted
through a specific message
One piece of information → different messages
Notes: Emphasize the asymmetry: the same information can be conveyed by different messages (different languages), and the same message can carry different information for different recipients.

## Slide 5
THE CONNECTING MECHANISM
The Rule of Interpretation φ
The link between message N and information I is given by a mapping φ: N → I
φ is the result of an agreement between the sender and the recipient of the message
"X understands the language" = X knows the interpretation rule for messages in that language
The rule may be known only to a limited circle: jargon, professional language, a cipher
In cryptography, φ is the "key": an outsider must not be able to recover it
N
message
φ
interpretation rule
I
information
φ(N) = I
Notes: Ask the class for an example where the interpretation rule is known only to a limited circle — jargon, cipher. Connect to cryptography: the key is the interpretation rule.

## Slide 6
LET’S WORK THROUGH THESE TOGETHER
Examples: Message ≠ Information
Inversion
"ylerpa" → read backwards → "april"
Caesar Cipher
Every letter shifted by 3 positions in the alphabet (Julius Caesar)
Steganography
A secret word hidden inside an "ordinary-looking" telegram text
Specialized Language
"e2-e4" — meaningful only to those who know chess notation
Takeaway: one rule φ — many possible messages; one piece of information — many ways to "package" it
Notes: Key interactive block. Work through each example out loud with the class, especially the Caesar cipher — invite students to encrypt a word on the board together.

## Slide 7
FROM SOURCE TO RECIPIENT
The General Scheme of Information Transmission
Source
Encoder
Converter
Communication
Channel
Decoder
Receiver
Noise / Interference
A communication line spans the entire path: from encoding the message to its reverse decoding
The source generates information and encodes it into a message (e.g., brain → language → speech)
The converter places the code onto a physical carrier (e.g., a modem)
The communication channel does not always faithfully reproduce every feature of the signal
Notes: Walk through the scheme left to right, asking "what has to happen next" before revealing each block. Give examples: the brain as source+encoder, a modem as converter, a telephone line as a bandwidth-limited channel.

## Slide 8
REAL-WORLD COMMUNICATION CHANNELS
Noise (Interference) and Protection
Any real communication channel is subject to external and internal influences
If the noise level is comparable to the signal intensity, transmission becomes impossible
Even relatively low noise levels can distort the transmitted signal
The task of coding theory is to develop methods of protection against interference
External Interference
Crosstalk from powerful electricity consumers, atmospheric phenomena, simultaneous action of several identical sources
Internal Interference
Physical inhomogeneity of the carrier, signal attenuation over long distances, parasitic effects
Protection: shielding communication lines, improving receiver selectivity, noise-resilient coding
Notes: Emphasize that fighting noise through coding — not just physical shielding — is the subject of upcoming lectures in this course.

## Slide 9
LOCKING IN THE TERMS
Rapid Review: 5 Key Concepts
Message
a concrete, material carrier of information
Information
what is extracted from a message through interpretation
Interpretation Rule φ
the correspondence between message N and information I
Noise (Interference)
a distorting influence on the signal in a communication channel
Coding
representing information as a sequence of symbols
Notes: Oral rapid-fire review: name the term, wait for the class to answer, then reveal the definition line by line. About 5 minutes for the whole block.

## Slide 10
WRAP-UP
What We Learned Today
1
Information is an undefinable primitive concept, like a point or a line in geometry
2
Message and information are linked through the interpretation rule φ: N → I
3
One piece of information — many messages; one message — many possible pieces of information
4
Communication system: source → encoder → converter → channel → decoder → receiver
5
Real channels are always subject to noise — hence the need for noise-resilient coding
Coming Up & Homework
Next lecture: the quantitative measure of information — the Hartley and Shannon formulas
Why the logarithm specifically underlies the measurement of information
Homework: prepare 2–3 of your own examples where the information is not obvious from the message
Thank you for your attention — questions?
Notes: Recap the takeaways out loud, connect to the next lecture (the Shannon formula), assign the homework, and leave time for questions.