## Slide 1
Information Characteristics & Capacity of Communication Channels
Lecture 5 • Comprehensive 50-Minute Guide for IT Students (Years 2–3)
Based on fundamental information theory: Bandwidth, Channel Matrices, and Shannon Entropies.

## Slide 2
LECTURE 5 • IT CHANNEL THEORY
Lecture Outline & Key Learning Modules (50 Minutes)
1. Physical Foundations (10 min)
• Channel bandwidth & frequency limits
• Maximum frequency fm & speed Vmax
• Elementary pulse duration tau0
• Pulse vs pause transmission constraints
2. Information Model (10 min)
• Statistical channel definition
• Input (X) and Output (Y) states
• Noise & signal distortion models
• Probabilistic graphs X -> Y
3. Channel Matrices (10 min)
• Source matrix P(Y|X) & row normalization
• Receiver matrix P(X|Y) & column sum
• Joint matrix P(X,Y) & marginals
• Interactive exercises
4. Entropies & Theorem (20 min)
• Entropies H(X), H(Y), H(Y|X), H(X|Y)
• Joint system entropy H(X,Y)
• Theorem on complete information set
• Review & homework assignment

## Slide 3
LECTURE 5 • IT CHANNEL THEORY
Concept of Communication Channel: Physical vs Information Approach
Physical Approach (Hardware)
• Focuses on physical transmission medium:
- Wires, fiber optics, radio spectrum
• Analyzes physical signals:
- Voltage, current, electromagnetic waves
• Primary constraints:
- Attenuation, dispersion, hardware noise
• Objective: High-fidelity wave propagation
Information Approach (Mathematical)
• Abstracts from hardware & voltage levels
• Models channel as a statistical transformer:
- Converts input symbols Xi to output Yj
• Focuses on probabilistic metrics:
- Error rates, mutual information, entropy
• Primary constraints:
- Shannon capacity limit, information loss
• Objective: Reliable symbol reconstruction

## Slide 4
LECTURE 5 • IT CHANNEL THEORY
Information Transmission Model: Source -> Channel -> Receiver
SOURCE (X)
Generates input symbols Xi with probabilities P(Xi) Alphabet size: N
CHANNEL + NOISE
Probabilistic mapping P(Y|X) Bandwidth limits Noise distorts Xi into Yj
RECEIVER (Y)
Registers output symbols Yj with probabilities P(Yj) Alphabet size: M
Key Architectural Principle
• Transmission is fundamentally statistical: Given input Xi, the output Yj is a random variable described by conditional probability P(Yj|Xi).

## Slide 5
LECTURE 5 • IT CHANNEL THEORY
Frequency Bandwidth of Communication Channels
Definition & Physical Constraints of Bandwidth
• Definition:
- Frequency bandwidth Delta_f = f_max - f_min is the frequency range that a channel passes without unacceptable attenuation.
• Physical Nature:
- Real channels (cables, optical fibers, air) act as frequency filters.
- High-frequency components undergo rapid attenuation and phase distortion.
• Real-World Bandwidth Examples:
- Standard telephone line: Delta_f = 3.1 kHz (300 Hz to 3400 Hz)
- High-quality audio channel: Delta_f = 20 kHz (20 Hz to 20 kHz)
- Optical cable channel: Delta_f > 1 GHz
• Key Takeaway for Information Theory:
- The upper cutoff frequency fm determines the maximum switching rate of signals!

## Slide 6
LECTURE 5 • IT CHANNEL THEORY
Maximum Frequency fm and Signaling Speed Limit
Physical Harmonical Relationship
• Harmonic period T = 1 / fm
• One full sine cycle T contains:
- One positive peak (Pulse)
- One negative trough (Pause)
• Thus, one period T can carry at most 2 elementary state transitions!
• Signaling rate formula:
Vmax = 2 * fm [symbols/sec or Baud]
Engineering Example & Calculation
• Example Problem:
- A communication channel has maximum frequency fm = 500 kHz.
- What is the maximum signaling speed Vmax?
• Solution:
- Vmax = 2 * fm = 2 * 500,000 = 1,000,000 Baud.
- The channel can transmit up to 1 Mbaud (1 million state transitions per second).
• Conclusion:
- Attempting to transmit faster than 2*fm forces signals to overlap and distort.

## Slide 7
LECTURE 5 • IT CHANNEL THEORY
Duration of Elementary Signal tau0 = 1 / (2 * fm)
Derivation of Elementary Pulse Duration tau0
• Mathematical Derivation:
- One full harmonic period T = 1 / fm.
- An elementary pulse corresponds to half a period: tau0 = T / 2.
- Substituting T gives: tau0 = 1 / (2 * fm).
• Physical Meaning:
- tau0 is the minimum time required for a physical signal to rise from zero to maximum amplitude and return.
• Numerical Example:
- If fm = 1 MHz (10^6 Hz), then tau0 = 1 / (2 * 10^6) = 0.5 microseconds (0.5 us).
- Any pulse shorter than 0.5 us will be heavily attenuated and lost in noise.

## Slide 8
LECTURE 5 • IT CHANNEL THEORY
Transmission of Pulses and Pauses: Duration Analysis
Scenario 1: Pulse Duration tau >= tau0
• Signal behavior:
- Pulse duration equals or exceeds minimum physical threshold tau0.
- Signal reaches full amplitude level.
• Transmission outcome:
- Receiver reliably distinguishes pulse from pause.
- Transmission rate is lower or equal to Vmax.
- Zero physical distortion error.
Scenario 2: Pulse Duration tau < tau0
• Signal behavior:
- Pulse is cut off before reaching full amplitude.
- Signal stays at intermediate voltage level.
• Transmission outcome:
- Inter-symbol interference (ISI) occurs.
- Receiver cannot distinguish pulse from pause.
- Inevitable information loss and high error rates!

## Slide 9
LECTURE 5 • IT CHANNEL THEORY
Information Model of a Channel as a Statistical System
5 Fundamental Probabilistic Parameter Sets
1. Input State Probabilities: P(X) = { P(x1), P(x2), ..., P(xN) }
- Unconditional probabilities of transmitter sending symbol Xi.
2. Output State Probabilities: P(Y) = { P(y1), P(y2), ..., P(yM) }
- Unconditional probabilities of receiver registering symbol Yj.
3. Source Channel Probabilities: P(Y|X) = [ P(yj|xi) ]
- Conditional probabilities of receiving Yj given that Xi was transmitted.
4. Receiver Channel Probabilities: P(X|Y) = [ P(xi|yj) ]
- Conditional probabilities that Xi was transmitted given that Yj was received.
5. Joint Probabilities: P(X,Y) = [ P(xi, yj) ]
- Absolute probabilities of transmitting Xi and receiving Yj simultaneously.

## Slide 10
LECTURE 5 • IT CHANNEL THEORY
Input and Output States: Sets X and Y
Input Ensemble X = {x1, x2, ..., xN}
• Complete group of events at source:
- Sum of P(xi) = 1 (i = 1..N)
• Alphabet size: N symbols
• Example (Binary Source):
- X = { x1='0', x2='1' }
- P(x1) = 0.6, P(x2) = 0.4
- Sum = 0.6 + 0.4 = 1.0
Output Ensemble Y = {y1, y2, ..., yM}
• Complete group of events at receiver:
- Sum of P(yj) = 1 (j = 1..M)
• Alphabet size: M symbols
• CRITICAL NOTE:
- N and M are NOT necessarily equal (N != M)!
- Example: Erasure channel has N=2 (0,1) and M=3 (0, 1, Erasure).

## Slide 11
LECTURE 5 • IT CHANNEL THEORY
Noise and Signal Distortion: Binary Symmetric Channel (BSC)
Binary Symmetric Channel (BSC) Model
• Definition of BSC:
- Binary input X={0,1} and binary output Y={0,1}.
- Error probability p = P(y=1|x=0) = P(y=0|x=1).
- Correct transmission probability 1-p = P(y=0|x=0) = P(y=1|x=1).
• Extreme Cases:
- Case p = 0: Ideal noiseless channel (100% reliable).
- Case p = 0.5: Pure noise channel (output is completely independent of input).
- Case p = 1.0: Inverting channel (deterministic inversion, 0 becomes 1).
• Probabilistic Mapping:
- Input x1='0' -> Output y1='0' (prob 1-p) OR y2='1' (prob p)
- Input x2='1' -> Output y1='0' (prob p) OR y2='1' (prob 1-p)

## Slide 12
LECTURE 5 • IT CHANNEL THEORY
Probabilistic Description: Source vs Receiver Perspective
Source Perspective Graph P(Y|X)
• Forward mapping:
- Arrows originate at input Xi and point to output Yj.
- Weighted by transition probabilities P(yj|xi).
• Engineering meaning:
- Answers: 'If I send Xi, where will it land?'
- Describes noise generation process in the channel.
Receiver Perspective Graph P(X|Y)
• Backward (A Posteriori) mapping:
- Arrows evaluate origin Xi given received Yj.
- Weighted by posterior probabilities P(xi|yj).
• Engineering meaning:
- Answers: 'Given received Yj, what was sent?'
- Describes decoding and decision making.

## Slide 13
LECTURE 5 • IT CHANNEL THEORY
Source Channel Matrix P(Y|X)
Matrix Structure & Definition
• Definition:
- P(Y|X) is an N x M matrix where row i represents transmitted Xi and column j represents received Yj.
• General Matrix Form:
P(Y|X) = [ P(y1|x1) P(y2|x1) ... P(yM|x1) ]
[ P(y1|x2) P(y2|x2) ... P(yM|x2) ]
[ ... ... ... ... ]
[ P(y1|xN) P(y2|xN) ... P(yM|xN) ]
• Physical Meaning:
- Diagonal elements P(yj|xi) with i=j represent correct transmission probabilities.
- Off-diagonal elements represent distortion/error probabilities.

## Slide 14
LECTURE 5 • IT CHANNEL THEORY
Properties of Source Channel Matrix P(Y|X)
Fundamental Mathematical Properties
• Property 1 (ROW NORMALIZATION RULE - MANDATORY):
- The sum of elements across ANY row i equals strictly 1.0:
Sum_j ( P(yj|xi) ) = 1.0 for every i = 1..N
- Proof: Transmitting Xi guarantees that SOME output Yj (j=1..M) will be received.
• Property 2 (Column Sum Constraint):
- The sum of elements down any column j is greater than zero:
Sum_i ( P(yj|xi) ) > 0 for every j = 1..M
- Meaning: Every output state Yj is reachable from at least one input state.
• Practical Verification Tip:
- If any row sum of P(Y|X) != 1.0, the calculation contains a fatal error!

## Slide 15
LECTURE 5 • IT CHANNEL THEORY
Interactive 1: Source Matrix Analysis (2-3 Minutes)
Exercise Problem
• Given Source Channel Matrix P(Y|X):
P(Y|X) = [ 0.85 0.15 ]
[ q 0.70 ]
• Questions:
1. Find unknown value q.
2. What is the error probability when transmitting x1?
3. What is the correct transmission probability for x2?
Solution for Instructor
• Solution Steps:
1. By Row Normalization Rule for Row 2:
q + 0.70 = 1.0 => q = 0.30.
2. Error when transmitting x1 is P(y2|x1) = 0.15 (15%).
3. Correct transmission for x2 is P(y2|x2) = 0.70 (70%).
• Completed Matrix:
P(Y|X) = [ 0.85 0.15 ]
[ 0.30 0.70 ]

## Slide 16
LECTURE 5 • IT CHANNEL THEORY
Receiver Channel Matrix P(X|Y)
Matrix Structure & A Posteriori Probabilities
• Definition:
- P(X|Y) is an N x M matrix of posterior probabilities P(xi|yj).
• General Matrix Form:
P(X|Y) = [ P(x1|y1) P(x1|y2) ... P(x1|yM) ]
[ P(x2|y1) P(x2|y2) ... P(x2|yM) ]
[ ... ... ... ... ]
[ P(xN|y1) P(xN|y2) ... P(xN|yM) ]
• Bayes' Rule Relation:
- P(xi|yj) = P(xi, yj) / P(yj) = [ P(xi) * P(yj|xi) ] / P(yj)
• Physical Meaning:
- Characterizes channel noise from receiver's point of view during decoding.

## Slide 17
LECTURE 5 • IT CHANNEL THEORY
Properties of Receiver Channel Matrix P(X|Y)
Column Normalization Rule
• Property 1 (COLUMN NORMALIZATION RULE - MANDATORY):
- The sum of elements down ANY column j equals strictly 1.0:
Sum_i ( P(xi|yj) ) = 1.0 for every j = 1..M
- Proof: Registering Yj implies that ONE of the input symbols Xi (i=1..N) was transmitted.
• Comparison of Matrix Properties:
- Source Matrix P(Y|X): ROW sum = 1.0
- Receiver Matrix P(X|Y): COLUMN sum = 1.0
• Key Takeaway:
- Never confuse row vs column normalization when verifying calculations!

## Slide 18
LECTURE 5 • IT CHANNEL THEORY
Joint Channel Matrix P(X,Y)
Joint Probabilities Structure
• Definition:
- P(X,Y) is an N x M matrix where element (i,j) is joint probability P(xi, yj).
• Fundamental Relations:
- P(xi, yj) = P(xi) * P(yj|xi) (via Source Matrix)
- P(xi, yj) = P(yj) * P(xi|yj) (via Receiver Matrix)
• General Matrix Form:
P(X,Y) = [ P(x1,y1) P(x1,y2) ... P(x1,yM) ]
[ P(x2,y1) P(x2,y2) ... P(x2,yM) ]
[ ... ... ... ... ]
[ P(xN,y1) P(xN,y2) ... P(xN,yM) ]
• Physical Meaning:
- Absolute probability of event pair (transmit Xi AND receive Yj).

## Slide 19
LECTURE 5 • IT CHANNEL THEORY
Properties of Joint Matrix P(X,Y) & Marginal Probabilities
3 Universal Properties of Joint Matrix
• Property 1 (TOTAL MATRIX NORMALIZATION):
- Sum of ALL elements in entire matrix equals 1.0:
Sum_i Sum_j ( P(xi, yj) ) = 1.0
• Property 2 (ROW SUMS = INPUT MARGINALS P(Xi)):
- Summing elements across row i gives input probability P(xi):
P(xi) = Sum_j ( P(xi, yj) )
• Property 3 (COLUMN SUMS = OUTPUT MARGINALS P(Yj)):
- Summing elements down column j gives output probability P(yj):
P(yj) = Sum_i ( P(xi, yj) )

## Slide 20
LECTURE 5 • IT CHANNEL THEORY
Interactive 2: Calculating Parameters from Joint Matrix (3-4 Minutes)
Exercise Problem
• Given Joint Matrix P(X,Y):
P(X,Y) = [ 0.40 0.10 ]
[ 0.05 0.45 ]
• Tasks:
1. Calculate input probabilities P(x1) and P(x2).
2. Calculate output probabilities P(y1) and P(y2).
3. Calculate error probability P(y2|x1).
Solution for Instructor
• Solution Steps:
1. Row sums for P(X):
P(x1) = 0.40 + 0.10 = 0.50; P(x2) = 0.05 + 0.45 = 0.50.
2. Column sums for P(Y):
P(y1) = 0.40 + 0.05 = 0.45; P(y2) = 0.10 + 0.45 = 0.55.
3. Conditional error probability P(y2|x1):
P(y2|x1) = P(x1, y2) / P(x1) = 0.10 / 0.50 = 0.20 (20%).

## Slide 21
LECTURE 5 • IT CHANNEL THEORY
Informationally Complete Set of Channel Characteristics
Definition & 5 Core Entropy Measures
• Definition of Informationally Complete Set:
- A set of parameters from which ANY other information property of the channel can be algebraically derived.
• The 5 Core Entropy Measures:
1. Source Entropy H(X): Unconditional transmitter uncertainty.
2. Receiver Entropy H(Y): Unconditional receiver uncertainty.
3. Noise Entropy H(Y|X): Equivocation (noise added by channel).
4. Loss Entropy H(X|Y): Receiver's uncertainty about sent symbol.
5. Joint Entropy H(X,Y): Total uncertainty of system (X,Y).

## Slide 22
LECTURE 5 • IT CHANNEL THEORY
Unconditional Entropies H(X) and H(Y)
Source Entropy H(X)
• Formula:
H(X) = - Sum_i ( P(xi) * log2 P(xi) )
• Meaning:
- Average information produced per source symbol.
• Maximum Value:
- Reached when all Xi are equiprobable: H_max = log2 N.
Receiver Entropy H(Y)
• Formula:
H(Y) = - Sum_j ( P(yj) * log2 P(yj) )
• Meaning:
- Average information received per output symbol.
• Note:
- Includes both useful information AND channel noise!

## Slide 23
LECTURE 5 • IT CHANNEL THEORY
Conditional Entropies H(Y|X) and H(X|Y): Noise & Losses
Noise Entropy H(Y|X) (Equivocation)
• Formula:
H(Y|X) = - Sum_i Sum_j ( P(xi, yj) * log2 P(yj|xi) )
• Physical Meaning:
- Measures NOISE introduced by the channel.
• In Noiseless Channel:
- H(Y|X) = 0 bits.
Loss Entropy H(X|Y) (Unreliability)
• Formula:
H(X|Y) = - Sum_i Sum_j ( P(xi, yj) * log2 P(xi|yj) )
• Physical Meaning:
- Measures INFORMATION LOSS (receiver doubt).
• In Lossless Channel:
- H(X|Y) = 0 bits.

## Slide 24
LECTURE 5 • IT CHANNEL THEORY
Joint System Entropy H(X,Y) & Balance Equations
Joint Entropy & Fundamental Entropy Balance
• Joint Entropy Formula:
H(X,Y) = - Sum_i Sum_j ( P(xi, yj) * log2 P(xi, yj) )
• Fundamental Entropy Balance Equations:
1. H(X,Y) = H(X) + H(Y|X) (Total Uncertainty = Source Info + Noise)
2. H(X,Y) = H(Y) + H(X|Y) (Total Uncertainty = Received Info + Loss)
• Transmitted Information (Mutual Information I(X;Y)):
I(X;Y) = H(X) - H(X|Y) = H(Y) - H(Y|X)
• Key Insight:
- Useful information transmitted equals Source Entropy minus Information Losses!

## Slide 25
LECTURE 5 • IT CHANNEL THEORY
Theorem on Informationally Complete Set
Theorem Statement & 3 Complete Variants
• Theorem Statement:
- An information parameter set containing ANY ONE of the following 3 options is an INFORMATIONALLY COMPLETE SET for the channel:
• Variant 1: Input probabilities P(X) AND Source Matrix P(Y|X)
• Variant 2: Output probabilities P(Y) AND Receiver Matrix P(X|Y)
• Variant 3: Joint Channel Matrix P(X,Y)
• Practical Importance:
- Engineers do not need to measure all 5 entropies individually; knowing Option 1, 2, or 3 allows exact algebraic calculation of all channel parameters!

## Slide 26
LECTURE 5 • IT CHANNEL THEORY
Proof of Theorem for Case 3 (Joint Matrix P(X,Y))
Step-by-Step Proof Demonstration
Given Joint Matrix P(X,Y), we systematically derive all channel parameters:
1. Derive Input Probabilities: P(xi) = Sum_j P(xi, yj) => Calculate H(X)
2. Derive Output Probabilities: P(yj) = Sum_i P(xi, yj) => Calculate H(Y)
3. Derive Source Matrix: P(yj|xi) = P(xi, yj) / P(xi) => Calculate H(Y|X)
4. Derive Receiver Matrix: P(xi|yj) = P(xi, yj) / P(yj) => Calculate H(X|Y)
5. Calculate Joint Entropy: H(X,Y) = - Sum_i Sum_j P(xi, yj) * log2 P(xi, yj)
Conclusion: Case 3 yields all 5 entropies and all matrices. Q.E.D.

## Slide 27
LECTURE 5 • IT CHANNEL THEORY
Summary & 5 Review Questions
Core Summary Points
1. Physical speed limit Vmax = 2*fm; tau0 = 1/(2*fm).
2. Source matrix P(Y|X): Row sum = 1.0.
3. Receiver matrix P(X|Y): Column sum = 1.0.
4. Joint matrix P(X,Y): Total sum = 1.0.
5. Joint matrix P(X,Y) is an informationally complete set.
5 Review Questions for Class
1. Why are pulses shorter than tau0 unacceptable?
2. What is the row sum rule for P(Y|X)?
3. What physical phenomenon does H(Y|X) represent?
4. How do you find P(X) from joint matrix P(X,Y)?
5. State the balance equation for H(X,Y).

## Slide 28
LECTURE 5 • IT CHANNEL THEORY
Homework Assignment & Final Remarks
Homework Assignment
1. Calculation Task 1 (Physical Limit):
- Compute tau0 and Vmax for channels with fm = 5 MHz and fm = 100 MHz.
2. Calculation Task 2 (Channel Matrices & Entropy):
- Given Joint Matrix P(X,Y) = [ 0.35 0.15 ] / [ 0.05 0.45 ]
- Find P(X), P(Y), Source Matrix P(Y|X), and Source Entropy H(X).
3. Theoretical Proof Task:
- Prove that for a noiseless channel, H(Y|X) = 0 and H(X,Y) = H(X).