## Slide 1
Fundamentals of Noise-Resistant Coding
Basic principles. Types of codes.
Notes: Plan: channel, principles, types of codes, Hamming (7,4), questions and tasks.

## Slide 2
Lecture plan
Why code? The noisy channel model
Basic principles: redundancy, Hamming distance, d_min
Types of codes: block, convolutional, linear, cyclic, modern
Worked example: Hamming (7,4)
Questions and practice tasks

## Slide 3
1. Why code? The noisy channel
Source → Source encoder → Channel encoder → Noisy channel → Decoder → Receiver
Binary symmetric channel (BSC): each bit flips with probability p
Shannon: if rate R < C, error probability can be made arbitrarily small
Source coding removes redundancy; channel coding adds controlled redundancy
Strategies: FEC (correct at receiver) and ARQ (retransmit)

## Slide 4
2. Basic principles
Redundancy: k info bits → n code bits; code rate R = k/n
Only 2^k of 2^n words are valid; the others reveal errors
Hamming distance d(a,b): number of differing positions
Detect s errors: d_min ≥ s + 1
Correct t errors: d_min ≥ 2t + 1
Decoding: choose the nearest valid codeword
Example: repetition code (3,1): 0→000, 1→111; d_min = 3 → corrects 1 error, R = 1/3

## Slide 5
3. Types of codes
Block (n,k) vs Convolutional
Convolutional codes use memory; Viterbi decoding
Linear
Generator G, parity-check H; syndrome s = H·rᵀ. Parity, Hamming
Cyclic
Polynomial-based: CRC, BCH, Reed–Solomon (CD, QR)
Modern
Turbo, LDPC (Wi-Fi, 5G), Polar (5G)
Also: systematic / non-systematic, detecting / correcting, binary / q-ary

## Slide 6
4. Hamming (7,4) code
Layout: p1 p2 d1 p4 d2 d3 d4 (even parity)
p1 checks positions 1,3,5,7 · p2: 2,3,6,7 · p4: 4,5,6,7
Data 1011 → codeword 0110011
Received 0110111: s1=1, s2=0, s4=1 → syndrome 101₂ = 5 → flip bit 5
R = 4/7, d_min = 3: detects 2 errors, corrects 1

## Slide 7
5. Questions
How does compression differ from error-control coding?
Can a single parity bit correct an error? Why?
If d_min = 5, how many errors are detected / corrected?
Why does the Hamming syndrome equal the error position?
Which code protects a QR code?

## Slide 8
6. Practice tasks
Find d(10110, 11100)
Even-parity bit for 1011001
Repetition code (3,1): decode 101
Encode 0110 with Hamming (7,4)
Received 1100100 (Hamming 7,4): find and fix the error
Homework: d_min of {00000, 01011, 10101, 11110}; encode 1001 with Hamming (7,4); short overview of CRC